## Slide 1: A Use-case Example: Transients
Demonstration on IEEE 123 bus system
8/14/2023
Oak Ridge National Laboratory
SI

## Slide 2
Transient Use-case a. Data Generation
  Objective: Development of an open-source transient data library
    Providing POW transient data in distribution models under multiple scenarios
    Developing algorithms for event detection and classification purpose, based on the datasets in the open-source data library

## Slide 3
Data generation
1584 fault cases in IEEE 123 bus system
Loading condition: 0.4/1.0
PV capacity: 0.4/0.6/0.8/1.0
Fault location: 3 ADJ + 63 three-phase buses
Fault type: single-phase/line-to-line/three-phase
Sampling rate: 20 kHz; Time window: [0s, 0.6s]
Data preprocessing
Avoid the initialization of simulation cases
Remove [0s, 0.2s] of the data
Topology of IEEE 123 bus system
Transient Use-case a. Data Generation

## Slide 4
  Methodology:
    Conducting data generation and preprocessing
    Developing waveform-based event detection algorithms
    Developing basic machine learning-based event classification algorithms
Transient Use-case b. Algorithms

## Slide 5
fault
PV trip
Detection
Classification
POW voltage
Event type
Data period with
detected event
Input Data: Detected event data period
  1584 fault cases (70% for training; 30% for testing)
Method: Multiple machine learning algorithms
Output: Identified event type as
  0 (single-phase) / 1 (line-to-line) / 2 (three-phase)
Confusion matrix of one ML algorithm (SVM)
Event detected?
Yes
No
Pass
No event detected
5 points after the event. (20 kHz sampling rate)
(a) Raw data
(b) DWT feature extraction
Input Data: POW phase A feeder head voltage of IEEE 123 bus network
  Loading condition: 0.4; PV capacity: 0.4
  Fault location: ADJ1
Method: Periodic waveform detector
Output: 0 (no event) / 1 (pass data during event period)
Transient Use-case b. Algorithms

## Slide 6
Data Generation
Data Preprocessing
Event Detection Algorithm
Event Classification Algorithm
Case number: 1584 fault cases in IEEE 123 bus system
Case variation: Loading condition/PV capacity/Fault type/Fault location
Sampling rate: 20kHz
Time window: 0~0.6s (event at 0.3s)
Remove initialization of the simulation (0~0.2s)
Method: periodic waveform detector
Threshold Selection: 0.012 (a. guarantee no misdetection; b. capture at the same point)
Data store: pre 0.05s and post 0.1s
Feature extraction: DWT method
Method: multiple machine learning algorithms
Class: Single-phase/line-to-line/three-phase fault
Data Processing
Transient analysis algorithm
Offline
Docker Package
Online
Naïve Bayes/SVM
Define model
Cross validation
Show results
Error, accuracy, time, confusion matrix
Transient Demo

## Slide 7
1. Open a terminal or command prompt, pull the docker image using the following command:
docker pull liub725/oedi-transient-demo
2. Run the Docker image using the following command which maps port 8888 of the container to the host's port 8888:
docker run -p 8888:8888 liub725/oedi-transient-demo
3. You should see the Jupyter Notebook server starting up. Look for a URL with a token in the terminal output, similar to:
http://127.0.0.1:8888/?token=<TOKEN>
4. Copy the URL and paste it into a web browser. This will open the Jupyter Notebook interface in your browser, where you can access and work with the notebook.
For demonstration, the preprocessed data are saved as csv files and directly loaded in the detection and classification Jupyter notebook examples.
Transient Demo